## Slide 1: DESIGN AND MODELLING OF MICROWAVE PLASMA REACTOR FOR THE PRODUCTION OF NANO-SILICON FROM QUARTZITE.
Presented by-
Sagar Kumar Das
Mydul Islam
Presented to-
Dr. Md. Fakhrul Islam
Professor
Dept of NCE, BUET
Date: 11th December 2023

## Slide 2
Whole task can be divided into 3 part
  Theoretical study
  Simulation
  Experiment

## Slide 3: THEORETICAL STUDY

## Slide 4: TE & TM Mode in Rectangular Waveguide
Here, TE mode is more significant for plasma generation.
Gas particles ionize in strong Electric field.

## Slide 5: Cut-off Frequency

## Slide 6: Different Types of TE mode
These modes depends on the dimensions of a waveguide.

## Slide 7: Size VS Frequency
As, Magnetron Frequency is 2.45GHz,so, WR340 basic dimensions have been chosen.

## Slide 8: Frequency Analysis
For TE mode, dominant mode is TE10 mode because of having lowest cut off frequency.
if, a=9cm & b=2cm
For TE10
fc,10 = 1.66 GHz
For TE20
fc,20 = 3.33GHz

## Slide 9
As suggested by Prof. Pradeep, IIT, India,
Operating frequncy (f0) should be at least 25% higher than TE10 mode and 5% less than TE20 mode.
So, actual operating region should be
1.25*fc,10 < f0 < 0.95*fc,20
As, in the lab, Magnetron frequency is f0 = 2.45GHz, the wave will operate on TE10 mode.
So we may choose ‘a = 9cm’ and ‘b=2cm for optimization case(according to the paper).

## Slide 10: Wavelength Analysis
Free Space Wavelength
λ = c/f0 = 126 mm
Guided Wavelength
λg = 167 mm
(λg /4) = 41mm ;
This is an important parameter for designing a 3dB waveguide design.

## Slide 11: LOW COST WAVEGUIDE MODEL

## Slide 12: Design with suggested dimensions
b
b
1.41*b
1.41*b

## Slide 13: Waveguide Parameters
LLeft
LRight
a
b
b = Height of the waveguide
a = Width of the waveguide
LRight = Length of the right arm.
LLeft = Length of the left arm.
At the beginning, a=90mm and b=20mm had been taken.
Plasma Chamber
λg /4

## Slide 14: SIMULATION

## Slide 15: Tolerance of Width ‘a’
Value of width b is very crucial for waveguide design as cut off frequency depends on it. Minor change during fabrication won’t cause any major issue as VSWR is within limit.

## Slide 16: Calculation of Right arm for lower VSWR
LRight
λguide /4+b
12mm
N*λguide /2
From the picture,
N*(λguide /2) = LRight + (λguide /4)+b – 12
83.4*N = LRight + 41.7+17-12
LRight = 83.4*N – 46.7
Here,
b = 17mm
λguide = 167mm
N = 2,3,4,5……..
For
N = 2; LR =120mm
N = 3; LR =204mm
N = 4; LR =287mm

## Slide 17: Calculation of Left arm for lower VSWR
Simulation shows that LRight has negligible impact on VSWR.

## Slide 18: Tolerance of Height ‘b’
17 mm has been chosen because of lower VSWR and Higher electric field intensity.

## Slide 19
15mm
17mm
23mm

## Slide 20: Favorable Dimensions after simulation
17mm
120mm
120mm
Without considering quartz tube, dimensions are given here.

## Slide 21: Waveguide Design Considering Air Tube
Radius of the tube has been taken 18mm.

## Slide 22: Impact of Air tube
There is visible impact of the tube on the waveguide.

## Slide 23: Practical Scenario Observation of the Magnetron side
Lower angle is showing better VSWR
Length of left arm is also impacting VSWR which was not in the previous model.

## Slide 24: Practical Scenario Observation of the Magnetron side

## Slide 25: Electric Field analysis

## Slide 26: EXPERIMENT

## Slide 27: Final Dimensions

## Slide 28: Necessary Connection and Equipments

## Slide 29: Waveguide after fabrication

## Slide 30: Full Set-up

## Slide 31: Test run and plasma