## Slide 1: Low Cost Waveguide Design

## Slide 2: TE & TM Mode in Rectangular Waveguide

## Slide 3: Cut-off Frequency

## Slide 4: Different Type of TE modes

## Slide 5: Size VS Frequency

## Slide 6: Calculation
For TE mode, dominant mode is TE10 mode because of having lowest cut off frequency.
From this equation,
fc,10 = 1.66 GHz if, a=9cm

## Slide 7: Calculation
In suggested model, b is taken as 2 cm.
So, the value of a/b > √3 which is over √3 than next dominant mode after TE10 is TE20 .
For TE20
fc,20 = 3.33GHz if, a=9cm
Magnetron having frequency of f0 = 2.45GHz
As, fc,10 < 2.45GHz < fc,20

## Slide 8: Suggested Model

## Slide 9: Suggested value of a and b

## Slide 11: Reflection Coefficient and VSWR
The range of values for VSWR is from 1 to ∞ . A VSWR value under 2 is considered suitable for most antenna applications. The antenna can be described as having a “Good Match”. So when someone says that the antenna is poorly matched, very often it means that the VSWR value exceeds 2 for a frequency of interest.

## Slide 12
Simulation Result

## Slide 13: Waveguide Design in HFSS
Left Arm(LF)
Right Arm(LR)
b
b + λguide /4
λguide /4

## Slide 14: Choosing the Value of a
a(mm) | S11 | VSWR
89 | 0.09 | 1.21
90 | 0.02 | 1.03
91 | 0.06 | 1.12
92 | 0.13 | 1.28
93 | 0.18 | 1.44
94 | 0.23 | 1.58
Here,
b=17mm, LF=150mm, LR=120mm

## Slide 15: Choosing value of Right Arm(LR)
LRight (mm) | S11(Reflection Coefficient) | VSWR
100 | 0.53 | 3.25
110 | 0.53 | 3.25
120 | 0.01 | 1.02
130 | 0.42 | 2.44
140 | 0.65 | 4.71
150 | 0.79 | 8.52
160 | 0.87 | 14.38
Acceptable value of VSWR is less than 2.
When,
a=90mm, b=17mm, LF=150mm

## Slide 17: Tolerance of Right Arm(LR)
LRight (mm) | S11 (Reflaction Coefficient) | VSWR
118 | 0.12 | 1.27
119 | 0.08 | 1.17
120 | 0.01 | 1.02
121 | 0.05 | 1.10
122 | 0.10 | 1.22
Here,
LR= 120+-(2) mm is showing VSWR is within limit.

## Slide 19: Choosing Value of Left Arm(LF)
LF(mm) | S11(Reflection Coefficient) | VSWR
100 | 0.02 | 1.04
120 | 0.02 | 1.04
140 | 0.01 | 1.02
160 | 0.01 | 1.02
180 | 0.02 | 1.04
According to simulation,
Left Arm(Magnetron Side) is showing there is negligible impact on VSWR.
When,
a=90mm, b=17mm, LR=120mm

## Slide 20: Choosing value of b
b(mm) | S11 (Reflection Coefficient) | VSWR
15 | 0.05 | 1.10
16 | 0.04 | 1.08
17 | 0.02 | 1.04
18 | 0.02 | 1.04
19 | 0.04 | 1.08
20 | 0.05 | 1.10
21 | 0.07 | 1.15
22 | 0.09 | 1.19
23 | 0.10 | 1.22
When,
a=90mm, LR=120mm, LF=150mm

## Slide 22: When b=15mm

## Slide 23: When b=17mm

## Slide 24: When b=23mm

## Slide 25: LR Value Calculation
N*λguide /2
λguide /4+b
12mm
approx.
LR
N*λguide /2 = LR + λguide /4+b – 12
83.4*N = LR + 41.7+17-12
LR = 83.4*N – 46.7 mm
For
N = 2; LR =120mm
N = 3; LR =204mm
N = 4; LR =287mm
*NB: Calculated value will provide lowest VSWR
Here,
b=17mm
λguide = 166.8 mm

## Slide 26: With LR=204mm & 287mm

## Slide 27: Checking by Simulation
LR | S11 | VSWR | Max E field (V/m)
120 | 0.01 | 1.02 | 75,945
204 | 0.03 | 1.06 | 77,170
287 | 0.02 | 1.04 | 76,712

## Slide 28: Discussion
According to the Simulation in Ansys HFSS,
we may choose,
a= 89-93 mm (for cut off freq)
b=15 to 20 mm ( Field intensity)
Right Arm = 83.4*N – 46.7 mm (b=17mm)
Left Arm = any (Negligible impact)

## Slide 29: Possible Difficulties in Practical Application
Fabrication error during making.
Impact of Quartz tube and it’s thickness.
Position of Magnetron.
Temperature and humidity.

## Slide 30: With Air Tube

## Slide 31: Electric Field

## Slide 32: Simulation Result
LR(mm) | Radius(mm) | Position of tube for wall(mm) | S11
120 | 18 | 41.7+5 | 0.49
125 | 18 | 41.7+5 | 0.26
130 | 18 | 41.7+5 | 0.09
135 | 18 | 41.7+5 | 0.32

## Slide 33: Effect of radius
Radius(mm) | LR(mm) |  | S11
18 | 130 |  | 0.09
12 | 130 |  | 0.33
12 | 125 |  | 0.12
5 | 125 |  | 0.24
5 | 120 |  | 0.03
0 | 120 |  | 0.02

## Slide 34: Practical POV of Magnetron side
Lower angle is showing better VSWR
Length of left arm is impacting VSWR which was not in the previous model.

## Slide 35: Thank You